## Slide 1: Coherent electron Cooling experiment at RHIC
Vladimir N Litvinenko
July 7, 2020

## Slide 2: CeC PCA Beamline
4-cell PCA
Modulator
Kicker
Unchanged
Unchanged
CeC SRF accelerator
New water-cooled solenoids
Dipoles gap modification
New Stands
New Profile Monitor
New BPM housing and buttons
12 Kicker-Modulator V/H Trims
New Y vacuum chamber for dipoles
New NEG coated beamline vacuum chambers
New stand supports for magnets
New RF shielded bellows
New conical transitions to RHIC
New beam line supports
Water Manifold for Solenoids
New replacement V/H trims for LEBT
Lead Shielding blocks
ATF Quads
Solenoid
Profile Monitor
BPM
V/H Trims
* Work in progress
* Completed

## Slide 3: 2020 Diagnostics Beamline
New High Power Beam Dump
New 1.3 GHz Transvers Deflecting Cavity
New Power Amplifier
New Profile Monitor YAGs (2)
New BPMs (2)
Re-use ERL Dipole
Re-use CeC Quads
Re-use CeC LE Beam Dump
New ICT
1.3 GHz Cavity
CeC Quads
ERL Dipole
LP Beam Dump
HP Beam Dump
CeC BPM
CeC PM

## Slide 4: Goals for Run 20
  Establish e-beam Key Performance Parameters (KPP)
    Milestone July 16, 2020
  Investigate Plasma Cascade Amplifier (PCA)
    Milestone – August 31, 2020
  Investigate Ion Imprint in the electron beam
    Milestone – September 30, 2020
  Because of the photocathode situation, we may interchange 2nd and 3rd milestones

## Slide 5: Establish e-beam KPP Nearly complete
Parameter | 
Lorentz factor | 28.5 v
Repetition frequency, kHz | 78.2 v
Electron beam full energy, MeV | 14.56 V
Total charge per bunch, nC | 1.5 V
Average beam current, μA | 117
Ratio of the noise power in the electron beam to the Poison noise limit | <100 V Need to verify
RMS momentum spread σp = σp/p, rms | ≤1.5×10-3 V
Normalized rms slice emittance, μm rad | ≤ 5 V

## Slide 6: Use of Dedicated time Total allocation for this Run is 8 days
This week 2 x 12 hrs (1 day)
  Complete KPP studies
  Develop RHIC ramp to 26.5 GeV/u
Rest of July (2 days)
  Establish beam dynamics in the PCA
  Establish BBA and orbit control in the common section
  Start investigation of PCA
August (3 days)
  Complete investigation of PCA
  Establish overlap of electron and Ion beams
  Start investigation of Ion imprint
September (2 days)
  Complete investigation of Ion imprint

## Slide 7: Additional factors
We may need to complete Fault studies of e-beam co-propagating with the ion beam in Yellow ring (new parallel mode of operation)
With current mode, we will request operations with abort gaps aligned at 2 o’clock (10% portion of time charged to the dedicated CeC mode)