## Slide 1: Preparation Status of pp Run11
Haixin Huang
Time Meeting
12/21/2010

## Slide 2: 250 GeV Run Machine Parameter
No of bunches: 109
Protons/bunch: 1.35x1011
Ramp working point Qx, Qy: (28.690,29.675)
Store working point Qx, Qy: (28.695,29.685)
# of collisions 2 (3 in later half store)
beta* for collisions 0.65 m @IP6& 8; 3m @ IP2
beta* for non collisions 7.5 m

## Slide 3: Critical Systems In Dry Run
Ramp System
  First test with the new ramp was successful (to the WFG level), more test will follow
RF application
  On going effort continues before the run starts.
RHIC Injection
  Teapot model server problem resolved(OS upgrade caused the problem). Additional work needs to be done to add code for smooth switch between 9/28MHz cavities and add spin check code.
RHIC CNI polarimeters
  Dry run for down stream polarimeter has finished. Dry run for upstream polarimeter will happen this week.
Tune/orbit feedback on the ramp
  Tune feedback is successful, orbit feedback will continue

## Slide 4: Schedule and New Items
Jan. 3-9 Cryo cool down, not much beam activity is expected.
Jan. 10-Jan. 27 two and half weeks RHIC setup.
Jan. 28- Feb. 4 ramp up mode, provide collisions overnight.
Feb. 5: Physics run starts.
New systems this year:
  9MHz cavity
  Beam dump upgrade (aperture smaller!)
  Upgraded spin flipper
  A robust tune/orbit/chromaticity feedback system
  Reversed BPM offsets
  Realigned RHIC ring vertically except section between 6-7.