## Slide 1: BLIP operations 03-1-11
Status – running at 117.5MeV
  BLIP weekly average beam increased to 102.5µA, highest this year. Operations dropped to 120.8 hours from planned shutdown to save cost in response to temporarily reduced demand for Sr-82 by the major user.
  Isotope production of Sr-82 has resumed, as secondary user has ramped up demand.
  Irradiation LBNE targets downstream of the isotope targets continues.
Operations issues
  Investigation of cause of Ga targets leaks continues.
    Linac will try again to get the octupole beam profile working in order to reduce power density on target. Literature indicates that the resistance of the Nb cladding to attack by Ga significantly declines at temperatures above 400 0C.
    We have begun investigating alternate cladding materials including Ta, W, alumina and graphite.

## Slide 2
Chart: To Date Accum. uA-hrs