## Slide 1: RHIC Status Update
Time Meeting
V. Schoefer
1/10/12

## Slide 2: Dry Run Summary
A successful dry run
    Problems were found, there is enough time to address them before the startup
Still a few major items waiting for full system check
  RHIC CNI motion control
  Tune/coupling and orbit feedback systems
    Can proceed once underlying work on wfgMan is complete
    Testing starting as early as tomorrow

## Slide 3: Start Up Outline
Start with 100 GeV protons (4 weeks of physics)
move later to 250 GeV (~5-7 weeks of physics)
Jan 17 : Start of final cooldown
Jan 21: Earliest injection into blue
  Followed by 9 MHz capture
  Instrumentation setup
Jan 24: Yellow injection
  Followed by 9 MHz capture
  Instrumentation setup
Jan 28: Power supplies ready for ramp
  Actual readiness for ramp depends on LLRF progress
Pacing item for startup/rampup is likely commissioning of LLRF changes and 9 MHz (no other major changes)
RF has a detailed shift-by-shift plan

## Slide 4: RHIC 100 GeV Polarized Proton Parameters
Parameters | Run 12 Goal
Interaction points | 6 8
* in blue [m] | 0.85 0.85
* in yellow [m] | 0.85 0.85
Working points (ramp and store) | 28.695, 29.685
Luminosity/Week | 10 pb-1 (max)
Polarization | 60-65%
Peak bunch intensity | 1.35  1011
Peak luminosity | 0.5  1032 cm-2s-1
No tune swing
Down from 1 m in Run 9

## Slide 5: RHIC 250 GeV Polarized Proton Parameters
Parameters | Run 11 Achieved | Run 12 Goal
Interaction points | 6 8 (AnDY test at 2) | 6 8
* in blue [m] | 0.8 0.6 | 0.65 0.65
* in yellow [m] | 0.65 0.63 | 0.65 0.65
Working points | Ramp: (28.680, 29.673) Store: (28.69, 29.68) | Ramp: (28.680, 29.673) Store: (28.69, 29.68)
Luminosity/Week | 25.4 pb-1 (the best, 4/5-12) | 40 pb-1 (max)
Polarization | 50%* | 55%
Peak bunch intensity | 1.65  1011 | 1.65  1011
Peak luminosity | 1.6  1032 cm-2s-1 | 2.0  1032 cm-2s-1
*Average of jet polarization is 46% for both rings. Taking into account for the polarization profile correction factor (R=0.2), The polarization seen by experimenters is boosted by Sqrt(1+R)=> 50%.
Notes: Peak luminosity goal nearly achieved, but at higher intensity than anticipated.
Higher intensity is a product of the 9 MHz cavity commissioning.
Problem is the emittance.