## Slide 1
Update on ions from EBIS
EBIS preinjector vs. EBIS source
- the source is meeting the design values
Running at > 10A electron beam. % in 32+ is lower than expected, but trap neutralization is higher (75%), and extended the length of the trap, so output from the source is good.
Transmission through the RFQ / MEBT / Linac is only ~70% of design.
  Multiple charge states in the beam, and not much space for diagnostics, makes it hard to determine the exact reason(s).
  Thought it was due to misalignment, but realignment didn't improve things, so still trying to understand.

## Slide 2
U to Booster input - expected ~ 93% of Au charge intensity ( 76% of particles in 39 vs. 32).
  Getting about 85% of expectation relative to Au (we think this just needs more tuning).
Booster - 85% capture/acceleration is as expected
Injection efficiency - thought 100%, getting 85%
  Emittance too large? need for faster orbit collapse?

## Slide 3
In addition, we now want to exceed the design intensity by ~30%
So (Au) - 0.77* 0.7 * 0.85 = 46% of where we‘d like to be
If we could get the ions out of EBIS in 1/2 turn (5us)....
could use 8 pulses to fill AGS instead of 4.
If this could be 100% efficient, we‘d get the factor of 2 we need.
RF setup for this 8 pulses is relatively ready.

## Slide 4
5 us pulse width is beyond what we ever intended for EBIS, so this is a work in progress.
Normal extraction

## Slide 5
Tried several ways to push ions out faster.

## Slide 6
Best so far is only 77% in 1/2 turn * 75% of the normal charge getting to the Booster (increased energy spread of ions out of EBIS as you push them out reduces transmission).
1
2
Continuing to refine the extraction.

## Slide 7
Energy spread out of Booster – looks good (0.3 eV-s)
Booster to AGS - for Au - ok.
For U, % stripped to 90+ after the Booster is lower than predicted (36% vs. ~50%), but still working on this. (stripping foil)
Bottom line -
Au – factor of ~2 minus whatever we gain from double pulsing
U – factor of ~3 minus gain from double pulsing (and stripper?)
Cu – should be a little better than Au, relative to requirement,