## Slide 1: Vernier scans RHIC run22
Online (“lisa”):
  No singles correction
  Only 1G fit
  Using model “bump”
Offline:
  Singles correction
  2G or 2G+const fit
  Model or BPM
    Moving ring only
    Both rings
Total of 14 scans
  High and low intensity
  28-111 bunches
  Gain x1 and x10
  Blue and Yellow
  3 different ramps

## Slide 2
33042 #1, 111x111 beta* 1.2 m, Y
Model (set) fits typically have better chi^2

## Slide 3
33042 #2, 111x111, beta* 1.0 m, Y
Discrepancy between model and set is evident regardless of rampfile

## Slide 4: Comparison vscan with IPM emittance
IPM scatter is rather large
Blue is typically larger than yellow
Expect vscan results between blue and yellow

## Slide 5: IPM and vscan (Hor)
Low intensity

## Slide 6: Beam-beam or electronic cross talk?
Low intensity: likely electronic cross talk
High intensity: Beam-beam
20 um
fixed
moving
Combine east&west

## Slide 7: ZDC effective cross section pp22-255GeV
Low intensity
Gain
x1
33172-sq1
1.86
Cross section should be constant regardless of beam conditions

## Slide 8: summary
Cross section should be constant:
  Only using “set” values satisfies this ‘rule’
Compare with independent measurement (IPM):
  “set” values give best agreement with IPM
  Rampfile does not appear to matter
Low intensity stores:
  No apparent beam-beam
  “set” and BPM agree within 5%
  Using both rings more ‘random’
BPM vs “set” consistent with beam-beam
  Intensity dependent
  Electronic cross talk and beam-beam evident
Using both rings AND correct gain gives best agreement also for high intensity stores (need to work on understanding gain calibration)
Conclude:
  Keep using “set” values
  Avg. of 1.86 mbarn