## Slide 1
RHIC Run 22 Startup Status 12/21/2021
Operating with two damaged coils in bi9 snake
  Second coil damaged on 12/12 (just prior to last time meeting)
  12/12-12/19
    Power supply/magnet group investigation of coil failure
    Rewiring of power supply to remaining two coils still allows operation as a partial snake
    Addition of UPS to both snake supply and associated controls
      Huge effort done safely and quickly.
    High current shutoffs did not find any problems with remaining coils
    Beam operation during this time: get to physics intensity levels without the blue snakes, ensure stable beam (higher than normal tune spreads).
  12/19: Recommission with partial snake
    ~4 hours to return to previously established store conditions, now with snake
  12/20, just beginning regular stores

## Slide 2
Collider performance with partial snake
Polarization
ZDC
Int. [1e11]
Run 17 full store avg polarization: 55%
  Yellow very close to Run 17: ~55%
  Blue: ~42% (pC full store average)
Partial snake causes
  Polarization Loss on injection into RHIC
  Lower polarization ramp transmission
  Store spin tilt and decay
Some improvement in ramp transmission ramping the partial snake to 320 A during acceleration.
  Higher current is overly lossy at injection energy
Bi9 snake: 300 A
Bi9 snake: 300->320 A

## Slide 3
Injection loss: modify rotation in 3 o’clock snake to compensate
  Higher current in the 9 o’clock snake also works, but increases losses on snake
Ramp transmission
  Orbit manipulations to counter snake imperfection
    mechanics still to be worked out
    In the plan for both rings for Run 22 prior to the helix damage
Store spin tilt/decay
  Measured ~20 deg tilt at pC polarimeter
  Possible global orbit manipulation to correct
    Uses imperfection resonance to rotate spin back
  Possibly use rotators to measure and correct longitudinal component at IP6
Plans for polarization improvements

## Slide 4
Other outstanding setup items
Luminosity still only up to 30% of required
  Discrepancy between expectation from Run 17 and what we measure (factor of 2 lower now, accounting for lower intensity)
    Large emittance?
    Vernier scan today or tomorrow.
Split/merge injector scheme
  Still needs some improvement in extracted bunch length to enable stable transfer to RHIC.